SIGNAL PROCESSING
FINAL PROJECT
Aniruth Suresh - 2022102055
Priya Mandot - 2022102053
Vishnuvarun - 2022102031

---
Lorem & Ipsum
INDEX
1. Echo Creation
2. Cancel The Echo
3.Classifying the Noise

---
1. Echo Creation
OBJECTIVE
Given that you are provided with an input audio file in a specific format .
Your task is to apply signal processing techniques to create an echo effect for the given audio.
.

---
1. Echo Creation
Simulating Natural Environment
Frequency of input
Surface Characteristics
Distance between source and the reflector
Time delay
.

---
1. Echo Creation
Any echo is of the form y[n] = x[n] + ɑ1 x[n-d1] + ɑ2 x[n-d2] + ...
We need to fix the attenuation factors and the delays and we can use the filter function or just manually append it.
.

---
2. Cancelling the Echo ( without the Desired Signal )
OBJECTIVE
We will be presented with an audio signal containing an echo with non-uniform delays.
Our task is to implement an echo cancellation algorithm to remove the echo components from the signal, leaving only the original, clean audio.
.

---
BASIC INTERPRETATION OF THE PROBLEM
Any echo is of the form y[n] = x[n] + ɑ1 x[n-d1] + ɑ2 x[n-d2] + ...
So , to extract the clean audio without the echo , we need to find the values of the attenuations ( ɑ ) and the exact values of the delay (ɑ)
Once we figure a way to find the value of ɑ and d , we can just use the inbuild – filter function in matlab to retrieve the pure original signal .
.

---
IMPLEMENTATION PROCESS
1. Perform AUTO – CORRELATION on the given corrupted signal .
2. Find attenuation factor and delay using the envelope function on the auto – correlated signal .
3. Use the inbuilt filter function whose arguments are numerator and denominator co – efficients .

---
1. AUTO CORRELATION
The autocorrelation function of a signal is defined as the measure of similarity or coherence between a signal and its time delayed version. Thus, the autocorrelation is the correlation of a signal with itself.
So , the peaks in the autocorrelation corresponds to the start of the delay ( cause original signal and the delayed signal overlapping similarity is higher )
This similarity keeps on reducing as the signal shifts towards the right .
( Consider only the right shift )

---
2.FINDING ATTENUATION FACTOR AND DELAY
Once we plot the Auto – correlated signal , we observe that the peaks correspond to the delay in the signal .
To get the corresponding x – values of those , we tried to use the inbuild matlab envelope function . But , this wasnt working properly cause the inbuild matlab code shifts the delay corresponding x value by some very small value ( 4-6 samples ) which results in irregular results .
So , we implemented own envelope function to get the delay start time .

---
IMPLEMENTING THE ENVELOPE FUNCTION
It is a standard envelope function which helps in finding the maximum of the different peaks by using a constant line ( p = e-λ) and keep reducing the λ to strengthen the function and to get multiple delays ( values corresponding to different peaks ) .
The points above the line when it cuts a peak are considered and separate analysis is run on them to make sure we get only a unique max point in a peak .
The analysis involves measuring the slope of these points and figuring the maximum out of them .

---
IMPLEMENTING THE ENVELOPE FUNCTION
We perform the same analysis on all the peaks and find the maximum of the next peak until the max of the peak is less than a specified cutoff .
We considered CUTOFF = Initial peak value / 25 .
We also make sure that the max of two peaks are not very close to each other , else this may result in irregular delays .
To overcome this , we explicitly force a condition that the minimum distance between any two peaks must be atleast 0.1 * Fs .

---
IMPLEMENTING THE ENVELOPE FUNCTION
Now we have all the start of delay values .
We now need to figure a way out to get the atteunation factor .
This can just be obtained by dividing the value of the max value of each peak with the maxmium peak of the entire auto – correlated function ( delay = 0 peak )
This is because at peak , max value corresponding to any peak is given by λS2 where S2 is the maximum value of the first peak .
We now divide both of these to get the λ ( attenuation factor ) .
So , we have figured out a way to calculate both delays and the attenuation factor .

---
3. FILTER FUNCTION
After getting the delays and attenuation factor , we use the filter function and get the num and den using the transfer function .
But this filter function in matlab computationally long but the output is filtered .

---
3.Classifying the Noise
OBJECTIVE
Our objective is to accurately identify and categorise the type of
noise present in the recording, distinguishing source of origin .